## Slide 1: The impact of low human intervention and other special features of A.I in the applicability of current legislation to A.I based medical devices
Amanda Näsi

## Slide 2: Element of trust in medicine
Fundamental concept due to the reliance of the patient upon healthcare
Diagnosis and treatment related decisions have impact on the patient’s life
Position of patients (Act on the Status and Rights of Patients 785/1992)
Safety of the patients is promoted in the Health Care Professionals Act (559/1994)
  To ensure the health care professionals are qualified and supervised
AI to be qualified and supervised too?

## Slide 3: Trustworthy AI
EU’s Commission’s High-Level Expert Group on Artificial Intelligence Ethics Guidelines for trustworthy AI
Requirements of trustworthy AI
  “Human agency and oversight
    Including fundamental rights, human agency and human oversight
  Technical robustness and safety
    Including resilience to attack and security, fall back plan and general safety, accuracy, reliability and reproducibility
  Privacy and data governance
    Including respect for privacy, quality and integrity of data, and access to data
  Transparency
    Including traceability, explainability and communication
  Diversity, non-discrimination and fairness
    Including the avoidance of unfair bias, accessibility and universal design, and stakeholder participation
  Societal and environmental wellbeing
    Including sustainability and environmental friendliness, social impact, society and democracy
  Accountability
    Including auditability, minimisation and reporting of negative impact, trade-offs and redress1”

## Slide 4: AI in medicine
How it is used?
  Convolutional neural network deep learning class
Where it is used?
  ECG analysis software
  Cancer imaging software
What is it?
  Medical device

## Slide 5: Medical Device Regulation/In-vitro Diagnostic Medical Devices Regulation
1990s
-Council Directive 90/385/EEC on Active Implantable Medical Devices (1990)
-Council Directive 93/42/EEC on Medical Devices (1993)
-Directive 98/79/EC of the European Parliament and of the Council on In vitro Diagnostic Medical Devices (1998)
2000s
-use of software as a medical device
2020s
-Medical Device Regulation (“MDR”, EU 2017/745) and the In-vitro Diagnostic Medical Devices Regulation (EU 2017/746)
-entered into force on May 2017
-replacement in phases (transition time)

## Slide 6: Manufacturer Case
You are  Manufacturing company in healthcare sector
You are developing  AI based software intended to perform a proposal of diagnosis of lung cancer by means of image analysis
You want  get into the market
According to article 10 (1) of MDR, when placing their devices on the market or putting them into service, manufacturers shall ensure that they have been designed and manufactured in accordance with the requirements of the MDR

## Slide 7: Definition of a medical device
“‘medical device’ means any instrument, apparatus, appliance, software, implant, reagent, material or other article intended by the manufacturer to be used, alone or in combination, for human beings for one or more of the following specific medical purposes:
  — diagnosis, prevention, monitoring, prediction, prognosis, treatment or alleviation of disease,
  — diagnosis, monitoring, treatment, alleviation of, or compensation for an injury or disability,
  — investigation, replacement or modification of the anatomy or of a physiological or pathological process or state,
  — providing information by means of in vitro examination of specimens derived from the human body, including organ, blood and tissue donations, and which does not achieve its principal intended action by pharmacological, immunological or metabolic means, in or on the human body, but which may be assisted in its function by such means. “(MDR, Article 2)

## Slide 8: Classification of medical devices -What class is our software in?
Rule 11 of MDR states as follows:
“Software intended to provide information which is used to take decisions with diagnosis or therapeutic purposes is classified as class IIa, except if such decisions have an impact that may cause:
— death or an irreversible deterioration of a person's state of health, in which case it is in class III; or
— a serious deterioration of a person's state of health or a surgical inter­vention, in which case it is classified as class IIb.
Software intended to monitor physiological processes is classified as class IIa, except if it is intended for monitoring of vital physiological parameters, where the nature of variations of those parameters is such that it could result in immediate danger to the patient, in which case it is classified as class IIb.
All other software is classified as class I.”

## Slide 9: General safety and performance requirements: Repeatability, reliability and performance
“Devices that incorporate electronic programmable systems, including software, or software that are devices in themselves, shall be designed to ensure repeatability, reliability and performance in line with their intended use.”(MDR Annex I, section 17.1)
Is our device repeatable, reliable and performing?

## Slide 10: Repeatability
Stability of outputs when the measurement conditions stay the same
Instead of repeatability, EU Committee on Legal Affairs has proposed AI operations to be “reproducible” due to its increased flexibility2”.
  Reproducibility
  “the ability to regenerate results using the original researchers' data, software, and parameters3”
Challenges of repeatability/reproducibility in AI software include:
        Reproducing the model requires training data is it available?
          Training data and the parameters must be stored accordingly and the training should be documented from the start of the development4

## Slide 11: Reliability
“Devices that incorporate electronic programmable systems, including software, or software that are devices in themselves, shall be designed to ensure …reliability…in line with their intended use.” (MDR Annex I, section 17.1)
Reliability in this context can be understood as “working properly with a range of inputs and in a range of situations5“
Sufficient training data

## Slide 12: Minimizing bias
“Bias is an inclination of prejudice towards or against a person, object, or position.6”
“The investigator's brochure (IB) shall contain details of measures to be taken to minimise bias, such as randomisation, and management of potential confounding factors” (MDR Annex XV Chapter II, section 3.6.4)
Taking into consideration different patient profiles

## Slide 13: Performing as ‘the state of the art’
“For devices that incorporate software or for software that are devices in themselves, the software shall be developed and manufactured in accordance with the state of the art taking into account the principles of development life cycle, risk management, including information security, verification and validation.” (MDR, Annex I, section 17.2)
  State of the art  latest technology
  Development life cycle  standards (e.g. IEC 62304)
  Risk management  MDR, Annex I, section 3
   AI specific risks?
  Verification and validation  MDR, Annex II, section 6

## Slide 14: Conclusion
Today we
  Went through some specific requirements of MDR from a viewpoint of manufacturer of AI based medical device
  Noticed that some of the requirements for trustworthy AI have been included in the MDR
    E.g. requirements for reliability, repeatability, performance, minimizing bias,
  Noticed that not all possible challenges of AI are reflected directly in the MDR
    Requirement for explainability
    Specific requirements for training data
Based on this
  MDR applies quite well to an AI based medical device which is used to support the decision making of the health care professional.
    Like in our example, the intended purpose of the device was to provide information which would be one of the “components” of decision making of the physician  not a decision maker
However, if in the future more autonomy is given to AI medical devices, the applicability and sufficiency of the current legislation might need revision.
For now according to section 2 (1) of the Act on Health Care Professionals “a health care professional is a person who, on the basis of this Act, has been given the right to practice a profession or the authorisation to practice a profession.”
Therefore due to the profession being subject to such license, AI, even if it could outperform the health care professionals, is not a health care professional itself (yet) and is regulated among other software as an important medical device.

## Slide 15: Thank you!

## Slide 16: Sources
Medical Device Regulation (MDR, EU 2017/745)
In-vitro Diagnostics Medical Devices Regulation (EU 2017/746)
Act on the Status and Rights of Patients (785/1992)
Act on Health Care Professionals (559/1994)
Medical Device Directive (93/42/EEC)
COCIR 2019.
    COCIR, the European Coordination Committee of the Radiological, Electromedical and Healthcare IT Industry, Artificial Intelligence in EU medical device legislation, September 2020. Available at: https://www.cocir.org/media-centre/publications/article/cocir-analysis-on-ai-in-medical-device-legislation-september-2020.html
Independent high-Level Expert Group on Artificial Intelligence set up by the European Commission 2019.
    Independent high-Level Expert Group on Artificial Intelligence set up by the European Commission, Ethics Guidelines for trustworthy AI, 8 April 2019. Available at: https://ec.europa.eu/digital-single-market/en/news/ethics-guidelines-trustworthy-ai
Hartley – Olsson 2020.
    Hartley, Matthew – Olsson, Tjellvar S.G. Patterns: dtoolAI: Reproducibility for Deep Learning, August 14, 2020. Available at: https://reader.elsevier.com/reader/sd/pii/S2666389920300933?token=BAF2BD9A63B521641E79FB4A25F954E3022331F033A0DD6F5B1A1369865D5CD7AD611AEBEF050A80B79296DCA6B468A7.
MDCG 2019.
    Guidance on Qualification and Classification of Software in Regulation (EU) 2017/745 – MDR and Regulation (EU) 2017/746 – IVDR, October 2019. Available at: https://ec.europa.eu/health/sites/health/files/md_topics-interest/docs/md_mdcg_2019_11_guidance_en.pdf
Committee on Legal Affairs 2020.
    Committee on Legal Affairs, Report with recommendations to the Commission on a framework of ethical aspects of artificial intelligence, robotics and related technologies 2020/2012(INL). Available at: https://www.europarl.europa.eu/doceo/document/A-9-2020-0186_EN.html

## Slide 17: Questions?